## Slide 1: (8,4,4) Viterbi Decoder
Group 2: Harsh Aurora, Adam Cavatassi, Xiaoqing Ma, Dylan Watts

## Slide 2: Overview
Background
  Encoding, transmission and decoding basics.
  Overview of the Viterbi (8,4,4) trellis.
Schematic and Layout
  Design overview of key modules.
  Implementation in schematic and layouts.
Testing
  Propagation Delay
  Power
Summary of Major Work
Future Work
References

## Slide 3: Background
Harsh Aurora

## Slide 4: Simplified Transmission Model
Information Source
Encoder
Modulator
Demodulator
Decoder
Information Sink
Channel
Transmitter
Receiver
[1011]
[10110010]
Output message bits
Message bits + error control
Transmission
pulses
Gaussian Noise Corruption
Pulse sampling
Message recovery
Input message bits
[1.3, 0.1, 0.5, 1.8, -0.2, 0.5, 0.9, 0.1]
[10X10X10]
[1011]

## Slide 5: Hamming (8,4,4) Encoder
Message:
Codeword:
Generator Matrix:

## Slide 6: Hamming (8,4,4) Encoder: Optimized Trellis
00
11
10
01
00
11
10
01
00
11
10
01
-
Example:
00/00
11/11
10/10
01/01
0/00
0/00
0/01
0/01
0/00
0/00
0/01
0/01
-/01
-/10
-/11
-/00
1/11
1/11
1/10
1/10
1/11
1/11
1/10
1/10
Start
End

## Slide 7: Modulator and Channel
BPSK modulation scheme:
Using this scheme, Codeword is modulated to the channel input
Channel:
Source of noise, characterized by Signal to Noise ratio (SNR)
where
Generate Gaussian distributed noise samples
Change the variance of the Gaussian to achieve different
The noisy channel observation is computed using

## Slide 8
Hamming (8,4,4)
Decoder
Maximum Likelihood decoder (MLE)
Best decoding performance!
Generate the codebook
All possible codewords for the 24 unique messages
Compute the distance between and each codeword
Most probable transmitted codeword =
  For all in the codebook
Computationally intensive!
(≈ 383 flops)
Aim: Retrieve the sent message , given the noisy channel observation
Figure 1: Maximum likelihood decoder performance.

## Slide 9
Hamming (8,4,4)
Decoder
Viterbi Decoder
Same performance as the MLE decoder!
Uses the Viterbi Algorithm on the Trellis
Calculate the shortest path of through the Trellis
The most likely is extracted from the shortest path
The modulation scheme and symmetry of the Trellis can further reduce the number of computations
(≈ 27 flops)
Figure 2: Comparison of Viterbi decoder with MLE decoder.

## Slide 10
Hamming (8,4,4)
Decoder
Start
End
Figure 3: Example of Hamming (8,4,4) trellis decoder.

## Slide 11
Hamming (8,4,4)
Decoder
Preparing for hardware: Use fixed point arithmetic for floating point operations!
An approximation of a floating point number
  Represent a signed floating point number as an () bit binary number
Define the fixed point format Qn.m, where
Fixed point arithmetic is implemented in the same manner as 2’s complement arithmetic
  With the exception that an overflow/underflow is handled by saturating the result at the maximum/minimum value of the Qn.m format
Fixed point arithmetic inherently produces quantization noise into the floating point calculations!

## Slide 12
Hamming (8,4,4)
Decoder
Obtain the performance of the Viterbi decoder for different Qn.m formats
Q3.10
Not enough integer range
Q4.2
Slight quantization noise
Q4.10
Greater fractional precision reduces noise, but at high cost (8 bits in this case)
Q6.2
Marginal improvements for greater integer range
Figure 4: Performance of various fixed point lengths

## Slide 13: Schematic and Layout
Adam Cavatassi, Xiaoqing Ma

## Slide 14: Design Summary
AMI 0.5μm process
MOSIS scalable CMOS submicron design rules
λ = 0.3μm

## Slide 15: Design Goals
Schematics and layout of 2 viterbi decoder
  Optimized for speed and power respectively
Schematics and layouts of related modules
DRC ERC NCC

## Slide 16: Required Modules
6-bit Adder
  Optimization for Speed: Kogge-Stone Adder
  Optimization for Power: Carry-Ripple Adder
6-bit Signed Number Comparator
6-bit Multiplexer

## Slide 17: Adder
6-bit signed binary addition
  If result < -32 (10000), output result as -32
  If result > 31 (01111), output result as 31
Overflow
  Check whether the result is out of range [-32, 31]

## Slide 18: Carry-Ripple Adder
Figure 5: Schematic and layout of 6-bit carry-ripple adder

## Slide 19: Carry-Ripple Adder
Figure 6: Schematic and layout of 6-bit carry-ripple adder

## Slide 20: Kogge-Stone (Tree Adder) – General Diagram
Figure 7 Reproduced from [1]: 16-bit kogge-stone adder PG networks

## Slide 21: Kogge-Stone (Tree Adder) – Bitwise PG Logic
Figure 8: Schematic and layout of bitwise PG logic

## Slide 22: Kogge-Stone (Tree Adder) – Group PG Logic
Figure 9: Schematic and layout of group PG logic (white cell)

## Slide 23: Kogge-Stone (Tree Adder) – Group PG Logic
Figure 10: Schematic and layout of group PG logic (black cell)

## Slide 24: Kogge-Stone (Tree Adder) – Overall Design
Bitwise PG Logic
Group PG Logic
Sum Logic
Rotate 90 Degrees Counterclockwise
Figure 11: Schematic and layout of 6-bit kogge-stone adder

## Slide 25: Kogge-Stone (Tree Adder) – Overall Design
Figure 12: Schematic and layout of 6-bit kogge-stone adder

## Slide 26: Comparator - Components
6-bit Carry-Ripple Adder
6-bit Inverter
1-bit XOR

## Slide 27: Comparator – Schematic and Layout
Figure 13: Schematic and layout of 6-bit comparator

## Slide 28: Miscellaneous
6-bit Multiplexer
  Consist of 6 1-bit multiplexers
  mux2_c_1x from standard cell library
6-bit Inverter
  Consist of 6 1-bit inverters
  Inv_1x from standard cell library

## Slide 29: Miscellaneous - 6-bit mux
Figure 14: Schematic and layout of 6-bit mux

## Slide 30: Miscellaneous - 6-bit inverter
Figure 15: Schematic and layout of 6-bit inverter

## Slide 31: Overall Design – Components
Module | Required Number
6-bit Adder | 18
6-bit Comparator | 11
6-bit Multiplexer | 10
1-bit Multiplexer | 12
1-bit Inverter | 6
Table 1: Number of individual modules

## Slide 32: Overall Design - Schematic
r0[5:0]
r1[5:0]
r2[5:0]
r4[5:0]
r6[5:0]
r7[5:0]
r5[5:0]
r3[5:0]
m[3:0]
Figure 16: Schematic of Viterbi decoder

## Slide 33: Overall Design – Layout (with CRA)
Figure 17: Layout of Viterbi decoder with carry-ripple adders

## Slide 34: Overall Design – Layout (with KSA)
Figure 18: Layout of Viterbi decoder with kogge-stone adders

## Slide 35: Testing
Harsh Aurora, Dylan Watts

## Slide 36: Logic Simulators
Harsh Aurora

## Slide 37: ModelSim
Functional verification of hardware designed in Electric
  Create a fixed point Viterbi Decoder in Verilog using ideal hardware components
  Extract noisy channel observations in Q4.2 format and the expected output from C code
  Build a testbench around the Verilog decoder implementation
    Using the extracted data from the C code
  Allow for incremental testing of hardware
    Substitute ideal Verilog components with Verilog code extracted from Electric
Figure 19: Example of functional testing via ModelSim

## Slide 38: Electric
All schematics and layouts passed DRC, ERC, NCC, as well as functionality testing through ModelSim and IRSIM
Figure 20: Demonstration of passing design checks for both decoder implementations.

## Slide 39: Circuit Simulators
Dylan Watts

## Slide 40: Challenges and Assumptions
Challenges:
  Circuit complexity – overall not a large circuit, but a lot of inputs.
  Licensing!!!!
Assumptions:
  Assume uniform distribution of input vectors – not true in general, but conservative.
  Neglect static power dissipation due to size of process, assume switching power is dominant factor.
  For the purposes of power calculation, each module drives a “characteristic capacitive load” which is a weighted average of interconnect and input capacitance.
  Delay of all outputs equal to the largest propagation delay for multi-output modules.
  False paths are neglected.
  Interconnect is neglected
  The transistor are uniformly sized using the “1x” ratio (between 1.5-2.5).

## Slide 41: Power Analysis
8 inputs of 6 bits each – Possible combinations are 248 = 281 trillion!
  Impractical to test all possible combinations of inputs and outputs in SPICE.
Can use a bounding approach.
  Test all possible combinations of input vectors for individual modules and observe the power statistics
  Min/avg/max power consumption.
Multiply individual statistics by the number of modules in the circuit.
By assuming every component in circuit is operating at the worst case input, can obtain a very conservative estimate of worst-case power consumption for the overall circuit.

## Slide 42: Power Analysis
Ripple-Carry and Kogge-Stone adder/comparator each take two six-bit input vectors:
  212 = 4096 possible input combinations.
2-input MUX takes two six-bit input vectors, 1 select line:
  Since it’s one or the other, can simplify to 1 six-bit input vector and one select line.
  27 = 128 possible input combinations.
Can generate these inputs intelligently by adding voltage pulses oscillating at specific frequencies:

## Slide 43: Power Analysis
Figure 21: Addition of periodic voltages to obtain desired waveform

## Slide 44: Power Analysis
Since each circuit is being evaluated independently, need to provide a “characteristic load”.
If interconnect is neglected, load is a combination of output capacitance and input capacitance of the connected module.
  Obtain a weighted average of input capacitance for all submodules
Table 2: Average and Maximum load capacitances/bit on each module.

## Slide 45: Power Simulation – adder6_KSA_avg
Figure 22: Spice simulation for all 4096 possible combinations

## Slide 46: Module Results – Average/Max Load
Table 3: Power usage of various sub-modules
Notes: Using netlists generated by electric and LTSPICE, an open source alternative to PSPICE and HSPICE we can analyze the power consumption of the four different modules.

## Slide 47: Circuit Results – Average/Max Load
Table 4: Power usage of the two decoder implementations under various loading conditions

## Slide 48: Propagation Delay: Static Timing Analysis
Can convert into a network of nodes and directed edges. The node weight corresponds to the delay of the component and the edge weight corresponds to the delay of the interconnect
Tools which can perform static timing analysis Cadence/Synopsis
Unfortunately had to make due with what was available – had to get creative.
Figure 23 Reproduced from [2]: conversion of logic paths into edge-weighted graph for calculation of shortest and longest path

## Slide 49: Static Timing Analysis
Gate Delay
Component Delay
Interconnect Delay
Circuit Delay
Delay of individual gates using built in RC timing simulator. Obtained using Electric and IRSIM.
Wire and gate delay combined into a node/edge weighted directed graph. Shortest/longest path algorithms run on Matlab.
Delay of wires connecting individual gates using a 4 segment -model. Obtained using Electric ‘Layout’ and LTSPICE.
Wire and component delay combined into a node/edge weighted directed graph. Shortest/longest path algorithms run on Matlab.

## Slide 50: Static Timing Analysis
Gate Delay
Component Delay
Interconnect Delay
Circuit Delay
Delay of individual gates using built in RC timing simulator. Obtained using Electric and IRSIM.
Wire and gate delay combined into a node/edge weighted directed graph. Shortest/longest path algorithms run on Matlab.
Delay of wires connecting individual gates using a 4 segment -model. Obtained using Electric ‘Layout’ and LTSPICE.
Wire and component delay combined into a node/edge weighted directed graph. Shortest/longest path algorithms run on Matlab.

## Slide 51: Individual Gate Delays
Typically provided by manufacturer
Can use IRSIM, a simulation program which uses rectangular waveforms, but takes into account an RC delay model
Figure 24: Propagation delay for a typical gate measured in IRSIM.

## Slide 52
Figure 25: Gate delays for all main foundational gates.

## Slide 53: Component Delay
With the gate delay and neglecting wire delay can determine longest/shortest path through various submodules, gradually moving up the hierarchy
Example: adder_ksa
Longest Path:
  Largest delay: adder6_ksa
  2 x Largest delay: MUX6
Shortest Path:
  Shortest path: inverter
  Shortest path: and3
  Shortest path:MUX6
Figure 25: Visual detection of longest ands shortest path

## Slide 54: Component Delay
Table 6: Delays for various sub-modules under various loading conditions.

## Slide 55: Circuit Delay
Once all submodules have been calculated for each circuit implementation, can determine the overall delay of the circuit:
Longest Path:
  3 x Largest delay: adder_ksa
  3 x Largest delay: comparator
  2 x Largest Delay: MUX6
  Largest delay: MUX2
Shortest Path:
  3 x shortest delay: adder_ksa
  Shortest delay: comparator
  Shortest delay: inverter
  2 x Shortest delay: MUX2
Figure 26: Visual detection of longest and shortest path.

## Slide 56: Circuit Delay
Table 7: Delay of decoder implementations under various loading conditions.

## Slide 57: Verify with Typical Cases - ISIM
Figure 27: Visualization of propagation delay and correct functionality of the circuit using IRSIM.
Can verify the validity of the bounds by running a full simulation of certain test vectors on IRSIM. As a byproduct, we can determine whether the circuit functions correctly!

## Slide 58: Circuit Delay

## Slide 59: Results Summary
Design Implementation:
  Both designs pass all relevant design checks (DRC, ERC,NCC)
Functionality:
  Both implementations function accordingly in both ModelSim and IRSIM.
Power Usage:
  The Kogge-Stone adder uses less power. (Topic of further investigation)
Propagation Delay:
  In 3 out of 4 cases Kogge-Stone is faster.
Table 8: Comparison of two decoder implementations.

## Slide 60: Summary of Major Work

## Slide 61: Summary of Major Work
Design of a custom architecture and data structure for the optimized encoding and decoding of (8,4,4) codewords.
Implementation of design of two different implementations, one optimized for speed and the other power, on both Schematic and Layout.
Full functional verification on ModelSim and partial verification on IRSIM.
Fulfillment of all design checks (DRC, ERC, NCC).
Exhaustive testing of decoder implementations under various loading regimens.
Determination of an upper and lower bound for power consumption and propagation delay.
Partial validation of upper and lower bound via IRSIM simulation.

## Slide 62: Future Work

## Slide 63: Future Work
Interconnect Delay
  Important to include – can account for up to 80% of overall delay of a circuit in modern processes [1].
  4 segment -model is sufficient to characterize the wire.
Comparator
  Replace the fulladder in the comparator with a Kogge-Stone adder. Should increase speed and reduce critical path.
Transistor Sizing
  Size the transistors to provide ideal ratio for propagation delay.

## Slide 64: References

## Slide 65
[1] CoN.West ad D.M. Harris, CMOS VLSI Design A Circuits and Systems Perspective, 4th ed., Addison-Wesley, 2011.
[2] VLSI Concepts, and online center for all who have interest in the Semiconductor industry; http://www.vlsi-expert.com/2011/03/static-timing-analysis-sta-basic-timing.html, Wed.March 9 2011.